## Slide 1: Ring Buffers
(Why software is hard)
Chris Lomont, 2019
chris@lomont.org
Notes: Also called FIFO queue, circular queue, bounded queue, others in literature

## Slide 2: Intro
This talk will cover a simple data structure, taken from the basic concept to production quality
It will illustrate a lot of tricks, nuances, and design tradeoffs
It illustrates that software is hard – the simple idea of a ring buffer is far removed from a production quality one

## Slide 3: Design purpose
I needed a ring buffer for an embedded project
Design needs
  An interrupt fills a ring buffer asynchronously from the main program
  Main program consumes data when available
  One or more physical CPUs (needed for Atmel SAMD21, Expressif ESP32)
  Very RAM conscious: the SAMD21 has 4K of RAM to implement a USB host
  High performance
  Standalone, reusable, modern C++ design principles
I found nothing available, created high performance Ring Buffer
Design and implementation illustrative of high and low level tricks

## Slide 4: Outline
Start with a simple design and implementation
Test to catch bugs
Make changes a little at a time to improve
10 different ring buffers, each better than the previous

## Slide 5: Simple Ring Buffer
State:
  Simple array size N to store data
  Next place to read is readIndex
  Next place to write is writeIndex
API roughly (actually, this is not the first I tried, but they evolved to this)
  bool IsEmpty
  bool IsFull
  int AvailableToRead
  int AvailableToWrite
  int Size
  bool Put(datum)
  bool Get(&datum)

## Slide 6: Simple Ring Buffer
bool Put(char datum)
{
if (IsFull()) return false;
buffer_[writeIndex_] = datum;
writeIndex_ = (writeIndex_ + 1) % size_;
return true;
}
bool Get(char & datum)
{
if (IsEmpty()) return false;
datum = buffer_[readIndex_];
readIndex_ = (readIndex_ + 1) % size_;
return true;
}
size_t size_;
uint32_t readIndex_{ 0 };
uint32_t writeIndex_{ 0 };
vector<char> buffer_;
size_t AvailableToRead() const
{
return (writeIndex_ - readIndex_ + size_) % size_;
}
size_t AvailableToWrite() const
{
return size_ - AvailableToRead();
}
bool IsEmpty() const { return AvailableToRead() == 0; }
bool IsFull() const { return AvailableToRead() == size_; }
size_t Size() const { return size_; }

## Slide 7: Simple Ring Buffer
Previous has multiple bugs: can you find them?
Can it really hold N items?
  Nope, it holds N-1. What to fix?
  Fix Size, AvailableToWrite, IsFull
Second much harder:
size_t size_;
uint32_t readIndex_{ 0 };
uint32_t writeIndex_{ 0 };
size_t AvailableToRead() const
{
return (writeIndex_ - readIndex_ + size_) % size_;
}
Full W=R-1
Empty W=R

## Slide 8: Simple Ring Buffer
size_t size_;
uint32_t readIndex_, writeIndex_;
(writeIndex_ - readIndex_ + size_) % size_;
Hint: this fixes: (size_ + writeIndex_ - readIndex_) % size_;
Also this: (static_cast<size_t>(writeIndex_) - readIndex_ + size_) % size_;
size_t is basically uint64_t
Order and promotion rules subtle.

## Slide 9: Simple Ring Buffer
C/C++ does not define over/underflow of signed integers
  So I designed using unsigned types
In this case: I encountered a wraparound of a size 513 buffer:
  write = 31, read = 512, math should then be write – read + 513 = 32,
    mod 513 should be 32.
Instead:
  write - read is -481 = 0xFFFF’FE1F as 32 bit hex,
  Add 32 bit unsigned to 64 bit unsigned size 513: 0xFFFF’FE1F expanded to 0x0000’0000’FFFF’FE1F, not 0xFFFF’FFFF’FFFF’FE1F
  Add to 513 = 0x0000’0000’0000’0201 as 64 bit hex,
  Obtain 0x0000’0001’0000’0020 as 64 bit hex. Note 1 way out there
  Now taking mod 513 returns 0, not 32!

## Slide 10: Generic Ring Buffer
Templatize items for flexibility
  Data type – can hold packets, etc.
  Size, allows compiler optimizations, can remove storing size as variable
    Downside – now multiple types GRB<32> versus GRB<64>, can subclass if needed
  Index type – allows smaller memory – don’t always need 32 bit index
template <size_t N = 512, typename DataType = char, typename IndexType = uint32_t>
class GenericRingBuffer

## Slide 11: Locked Ring Buffer
Need to make threadsafe
  Use locks, C++11 to C++17 ok.
API now dangerous and flakey
  For example, int AvailableToRead not safe under multiple readers
  Could relabel, or could remove or rethink
  Safer to simply kill bad named functions

## Slide 12: Locked Ring Buffer
using Scoped = lock_guard<recursive_mutex>;
…
bool Put(const DataType & datum)
{
Scoped guard(lock_);
if (IsFull())
return false;
buffer_[writeIndex_] = datum;
writeIndex_ = (writeIndex_ + 1) % N;
return true;
}
…
mutable recursive_mutex lock_;
Locking guidelines
  simply using mutex hangs, use recursive_mutex.
  Use scope guards for exceptions
  Need mutable lock for const members,
  ugly, must be careful to meet const for classes how C++ expects them

## Slide 13: Benchmarking
First benchmarks:
  One thread, ring buffer size N, write M, read M in loop
  Two threads, same as above, in 2 threads
  Cannot compare throughput between 1 and 2 easily!
Want about 30-50 ms per sample on Windows (15 ms thread slices)
  Lower, hit numeric issues
  Higher, don’t get more info, just slower to test
  Want enough OS thread slices overall to gather good avg data
Intel Core i7, Visual Studio 2017 C++, x64, Release mode.
TODO - Atmel SAMD21, GCC Atmel7 studio

## Slide 14: Performance I
Note sizes near power of 2 speeds
Chart: One thread, MB/s, buffer size
| 29 | 32 | 50 | 128
Simple | 95.3 | 130 | 95.3 | 130
Generic | 150.5 | 572.2 | 150.5 | 572.2
Locked | 13.9 | 12.7 | 13.6 | 13.9
Chart: Near power of 2
| 126 | 127 | 128 | 129 | 130
Simple | 95.3 | 95.3 | 124.3 | 105.9 | 105.9
Generic | 150.5 | 150.5 | 572.2 | 204.3 | 204.3

## Slide 15: Performance I
Hint: 10 * (2^31) / 123 = 174592166.504

## Slide 16: Atomics Ring Buffer
We have one writer (interrupt), one reader (main loop)
This called a Single Producer, Single Consumer (SPSC) Ring Buffer
Also have SPMC, MPMC, MPSC, etc.
Can redo API nicely:
// how many items available to write in [0,Size]
// if called from consumer, true size may be less since producer can be adding
// if called from producer, true size may be more since consumer may be removing
// undefined to call from any other thread
size_t AvailableToWrite() const { return Size() - AvailableToRead(); }
atomic<IndexType> readIndex_{ 0 };
atomic<IndexType> writeIndex_{ 0 };
array<DataType, N> buffer_;

## Slide 17: Atomics Ring Buffer
We can replace locking with std::atomics
Read each at most once per function, same order safest
Best to read papers instead of making your own:
  Lamport paper 1977
// try to put the item in, return false if full
bool Put(const DataType & datum)
{
IndexType w = writeIndex_;
IndexType r = readIndex_;
if ((w+1)%N == r)
return false;
buffer_[w] = datum;
writeIndex_ = (w + 1) % N;
return true;
}
Notes: Correct and Efficient Bounded FIFO Queues, https://www.irif.fr/~guatto/papers/sbac13.pdf

## Slide 18: Performance 2
Atomic vastly faster than locked, single or double threads
Chart: One thread MB/s by ring size
| 29 | 32 | 50 | 128
Generic | 150.5 | 572.2 | 150.5 | 572.2
Locked | 13.9 | 13.9 | 14.3 | 14.3
Atomic | 52 | 62.1 | 52 | 62.1
Chart: Two thread, MB/s for size 128
| Locked | Atomic
128 | 0.2 | 13

## Slide 19: Modulus Ring Buffer
Modulus % is computationally expensive.
Our values should stay in 0 to N-1
% for N power of 2 is very cheap: simply AND mask with N-1
Replace % with ‘if’
  Trades expensive % with possibly expensive branch
Want template magic to select which at compile time
template <..., typename RingMod> class ModulusRingBuffer { ...
size_t AvailableToRead() {
return RingMod::Mod1N(N + writeIndex_ - readIndex_); }
...
// template to detect if N is power of 2
template<size_t N> struct is_power_of_two {
static const bool value = N && ((N & (N - 1)) == 0);};
// pick based on power of 2 or not
template<size_t N, typename IndexType>
using FastRingMod = conditional_t<is_power_of_two<N>::value,
FastRingModPowerOfTwo<N, IndexType>,
MidRingMod<N, IndexType>
>;

## Slide 20: Modulus Ring Buffer
template<size_t N, typename IndexType>
struct MidRingMod {
// given integer in [0,2N-1], return mod N in [0,N-1]
static inline IndexType Mod1N(const IndexType & index)
{
if (index < N) return index;
return index - N;
}};
...
SlowRingMod => return index % N;
FastRingModPowerOfTwo => return index & (N - 1);

## Slide 21: Relaxed Ring Buffer
CPU, compiler, and language memory models allow reordering loads and stores across threads and caches.
C++ atomic forces strict sequential ordering
  sequential consistency => 1) Each thread ordered, 2) overall order is total ordered
Relax => Replace default atomic read/write with weakest correct requirement
VERY hard to get correct!
C++ atomics memory_order_... | Meaning
acquire | All following loads not moved before any current or preceding loads
release | All preceding stores not moved past any current or later stores
acq_rel | Does both acquire and release
consume | Weaker form of acquire, only does acquire on data dependent loads
relaxed | All reorderings ok
seq_cst | Default: sequential consistency
Notes: Remark: best to find a paper, then scan papers citing it to see if improvements/corrections
Difference between seq_cst and acq_rel is latter is only relative to the sinlge atomic variable, seq_cst is global.
i.e. Seq_cst is across all threads

## Slide 22: Relaxed Ring Buffer
// try to put the item in, return false if full
bool Put(const DataType & datum)
{
IndexType w = writeIndex_.load(memory_order_relaxed);
const IndexType nextWrite = RingMod::Mod1N(w + 1);
if (nextWrite != readIndex_.load(memory_order_acquire))
{
buffer_[w] = datum;
writeIndex_.store(nextWrite, memory_order_release);
return true;
}
return false; // buffer full
}
Note: branching order changed to often better choice - most taken closest

## Slide 23: Performance 3
Chart: Single thread MB/s
| Atomic | SlowMod | MidMod | FastMod
127 | 52 | 52 | 62.1 | 62.1
128 | 62.1 | 62.1 | 62.1 | 62.1
129 | 56 | 56 | 62.1 | 62.1
Chart: Single Thread MB/s
| 29 | 32 | 50 | 128
Atomic | 52 | 62.1 | 52 | 62.1
FastMod | 62.1 | 62.1 | 62.1 | 62.1
Relaxed | 357.6 | 476.8 | 357.6 | 476.8
Chart: Double thread MB/s
| 29 | 32 | 50 | 128
Atomic | 11.9 | 11.9 | 11.5 | 10.8
FastMod | 11.5 | 11.9 | 11.9 | 10.8
Relaxed | 19.3 | 19.8 | 19.3 | 19.3

## Slide 24: Full Size Buffer
Want to use all N slots in low memory device
read=write cannot both mark empty and full
Thus need another field to track which is which
A separate field is tricky to get right with atomics
Nice trick: instead of using numbers mod N, take them mod 2N
  Gives another ‘bit’ of information to split full/empty cases
Downside: need an extra mod N during buffer read/write

## Slide 25: Full Size Buffer
// try to write an element, fails if no space available
bool Put(const DataType & datum)
{ // paper above has ability to write bigger blocks, is faster
const auto w = writeIndex_.load(memory_order_relaxed);
const auto nextWrite = RingMod::Mod2N(w + 1);
if (nextWrite != readIndex_.load(memory_order_acquire))
{
buffer_[RingMod::Mod1N(w)] = datum;
writeIndex_.store(nextWrite, memory_order_release);
return true;
}
return false; // buffer full
}

## Slide 26: Cache Ring Buffer
False sharing
  Things close in memory but used by different threads
  Either thread reads cache line, must read both items
  Thrashes
Move lines around to put space between things for different threads
Can do better, greater cost…
atomic<IndexType> writeIndex_{ 0 };
array<DataType, N> buffer_;
atomic<IndexType> readIndex_{ 0 };

## Slide 27: Blocks Ring Buffer
Most times one wants to write a block of bytes in
Often want to read a block out
Can avoid so many atomic hits by doing things in blocks
Add new APIs
  bool Put(DataType * data, size_t n)
  bool Get(DataType * data, size_t n)

## Slide 28: Blocks Ring Buffer
// try to write n elements, fails if no space available
bool Put(const DataType * data, size_t n)
{
auto w = writeIndex_.load(memory_order_relaxed);
auto r = readIndex_.load(memory_order_acquire);
if (Size() - RingMod::Mod2N(2 * N + w - r) < n)
return false; // does not fit
auto t = RingMod::Mod1N(w);
for (auto i = 0; i < n; ++i)
buffer_[RingMod::Mod1N(t+i)] = data[i];
w = RingMod::Mod2N(w + n);
writeIndex_.store(w, memory_order_release);
return true;
}
Notes: TODO – can possibly change to not use 2 mod per loop – mod in array w+i, then out of loop mod2n final w+n – errors – why? Possibly can split into values that stay in bounds, and do those – remove all per loop mod

## Slide 29: Predictive Ring Buffer (final buffer)
Can avoid some atomic checks by caching a non-atomic value on each of producer/consumer side
Adds memory cost of two more counters
Improves performance on some architectures
// predictive read index, cache neighbors
IndexType pReadIndex_{ 0 };
atomic<IndexType> writeIndex_{ 0 };
DataType buffer_[N];
// predictive write index, cache neighbors
IndexType pWriteIndex_{ 0 };
atomic<IndexType> readIndex_{ 0 };
Notes: Paper WeakRB
Paper shows only 1.25% of possible throughout on ARM, 0.6% on PC
WeakRB
  Software caches to prevent multiple needs to check atomic

## Slide 30: Predictive Ring Buffer (final buffer)
bool Put(const DataType * data, size_t n)
{
auto w = writeIndex_.load(...);
// predicted available to write
if ( Size() - RingMod::Mod2N(2 * N + w - pReadIndex_) < n)
{ // may not fit, check more exactly, costing an atomic read
pReadIndex_ = readIndex_.load(...);
// current available to write
if (Size() - RingMod::Mod2N(2 * N + w - pReadIndex_) < n)
return false; // does not fit
}
...

## Slide 31: Performance 4
Relaxed, full buffer, large blocks, cache lines, predictive
Chart: Single thread MB/s
| Relaxed | Full | Cache | Blocks | Predictive
29 | 363.3 | 305.1 | 305.1 | 305.1 | 317.8
32 | 476.8 | 448.7 | 448.7 | 448.7 | 448.7
50 | 363.3 | 305.1 | 305.1 | 305.1 | 331.7
128 | 476.8 | 508.6 | 508.6 | 508.6 | 508.6
Chart: Two threads MB/s
| Relaxed | Full | Cache | Blocks | Predictive
29 | 20 | 19.5 | 19.5 | 19.5 | 19.5
32 | 19.5 | 19.5 | 20 | 20 | 19.5
50 | 20 | 20 | 19 | 19.5 | 19
128 | 20 | 20 | 20 | 20 | 20.6

## Slide 32: Performance 5
Blocks vs predictive
  note: carefully rewriting inner loop lifted values from 1100 to 1500
Chart: Block throughput, one and two threads
| Single | Single block | Double | Double block
Blocks | 497.5 | 1226.1 | 19.2 | 246.1
Predictive | 497.5 | 1492.7 | 21.1 | 254.3

## Slide 33: Correctness?
Extremely hard to prove correctness
Can stress test like crazy
Relacy Race Detector - header library to stress
  Automatically does reorderings and tries to crash programs
  Simply include “relacy.hpp”, replace std:: with rl::, and access vars of interest with suffix ($)
  Can do with macros cleanly
Ran significant tests on final ring.

## Slide 34: Looking at generated assembly – very compact

## Slide 35: Performance 6
Chart: One thread MB/s
Simple | 130
Generic | 560.9
Locks | 13.6
Atomics | 63.5
Modulus | 63.5
Relaxed | 476.8
Full | 501.9
Cache | 501.9
Blocks | 1192
Predictive | 1467.1
Chart: Two thread MB/s
Locks | 0.2
Atomics | 11.9
Modulus | 11.9
Relaxed | 20
Full | 21.1
Cache | 22.4
Blocks | 272.4
Predictive | 254.3

## Slide 36: Performance 7
Chart: Atmel SAMD21, Single test Byte and block methods kB/s
Simple | 1713.2675
Generic | 1713.2675
Locked | 1713.2675
Atomics | 561.2428
Mod Slow | 542.5347
Mod Mid | 551.7302
Mod Fast | 536.5728
Relaxed | 1302.0833
Full | 1236.1551
Cache | 1236.1551
Blocks | 1236.1551
Pred | 1236.1551

## Slide 37: Conclusion
List of all improvement ideas and gain over previous:
  Initial implementation
  Made parameters generic to gain compiler optimizations
  Made threaded with locks
  Replaced locks with careful atomics
  Replaced modulus with if and bitmask and template tricks
  Replaced seq_cst atomics with careful load/store semantics
  Replaced N-1 buffer with full N buffer via mod 2N math
  Tried to arrange data for better cache and non-false sharing
  Changed API to handle blocks instead of single put/get
  Removed some cache sharing via predictive size buffering